TOPIC 3: MODULATION AND ENCODING

Data must be transformed into signals to send them from one place to another.

# Conversion Scheme

- Digital-to-Digital

- Analog-to-Digital

- Digital-to-Analog

- Analog-to-Analog

  - Digital-to-Digital Encoding – representation of digital information by a digital signal

Types of D/D encoding:

    - Unipolar – simplest yet primitive; uses only one level of value; straight forward & inexpensive to implement.

Unipolar encoding is less desirable because of::

      - Presence of DC component – average amplitude of a unipolar encoded signal is nonzero (creating a DC); it cannot travel to a media that can’t handle DC.

      - Synchronization – occurs in unipolar encoding when the receiver can’t determine the beginning and ending of each bit thereby distorting the timing of the signal.

    - Polar – uses 2 levels (+ or -) of amplitude

Types:

- Non return to Zero (NRZ) – level of signal is always either (+) or (-)

### Forms of NRZ transmission

  - NRZ-L – the level of signal is dependent upon the state of the bit; positive voltage means 0; negative means the bit is 1.

  - NRZ-I – an inversion of the voltage level represents a 1 bit.  It is transition between a (+) and a (-) voltage, not the voltage themselves, that represents a 1 bit.  A 0 bit represents no change.

- Return to Zero (RZ) – uses 3 values: positive, negative or zero.

Advantage: assurance of synchronization

Disadvantage: requires 2 signal changes to encode one bit, occupying more BW.

- Biphase – provides the best solution for synchronization problems; the signal changes at the middle of the bit interval but does not return to zero.  Instead, it continues to the opposite pole.

Implemented by

  - Manchester encoding – the transition at the middle of the bit is used for both synchronization & bit representation.

  - Differential Manchester – the transition at the middle of the bit is used only for synchronization. The bit representation is shown by the inversion or non-inversion at the beginning of the bit.

    - Bipolar – uses 3 voltage levels like the RZ; zero level is used to represent binary 0; the 1s are represented by alternating (+) & (-) voltages.

Types of bipolar encoding:

- Alternate Mark Inversion (AMI) – simplest type of bipolar encoding; A zero voltage represents binary zero; 1s are represented by alternating (+) & (-) voltages.

* By inverting on each occurrence of a 1, bipolar AMI accomplishes two things:

first, DC component is zero and second, a long sequence of 1s  stays synchronized.

* No mechanism to ensure synchronization of a long string of one’s.

Solutions: Bipolar 8 – Zero Substitution ( B8ZS) & High- Density Bipolar 3 (HDB3)

- Bipolar 8 – Zero Substitution ( B8ZS) – convention adopted in N. America to provide synchronization of long strings of 0s.

  - forces artificial signal changes, called violations, w/ in the Ø string.

  - Anytime eight 0s occur in succession, B8ZS introduces changes in the pattern based on the polarity of the previous 1.

- High- Density Bipolar 3 (HDB3) – used in Japan & Europe

  - in HDB3, if 4 0’s come one after another, we change the pattern in one of four ways based  on the polarity pf the previous 1 and the no. of 1s since the last substitution.

## II. ANALOG- TO- DIGITAL CONVERSION

PULSE  AMPLITUDE MODULATION (PAM) – first  step in analog- to- digital conversion; foundation of PCM

PULSE CODE MODULATION (PCM) – made up of 4 processes: PAM, quantization; binary encoding & digital- to- digital encoding

Quantization- method of assigning integral values in a specific range to sampled instances.

Nyquist theorem: The sampling rate must be at least two times the highest frequency.

## III. DIGITAL-TO-ANALOG CONVERSION

- process of changing one of the characteristics of an analog signal based on the information in a digital signal.

Bit rate – no. of bits transmitted per second.

Baud - no. of signal units per second.

*Baud is less than or equal to the bit rate.

Types:

- Amplitude Shift Keying (ASK) – the strength of the carrier signal is varied to represent binary 1 and 0.

- highly susceptible  to noise and interference; modulating method most affected by noise.

On-off keying (OOK) – most popular ASK technique; known to some as digital AM.

- Frequency Shift Keying(FSK) - freq, of carrier signal is varied to represent binary 1 and 0.

- Phase Shift Keying (PSK) – phase of the carrier is varied to represent binary 1 and 0.

  - BPSK or (2-PSK)

  - QPSK or (4- PSK)

  - 8-PSK

- Quadrature Amplitude Modulation (QAM) means combining ASK & PSK in such a way that we have maximum contrast b/w each bit, dibit, tribit, etc.

  - 4- QAM

  - 8-QAM

  - 16- QAM

## Bit / Baud Comparison

| Modulation | Units | Bits | Bit rate | Baud (rate) |
| --- | --- | --- | --- | --- |
| ASK, FSK, BPSK | Bit | 1 | N | N |
| 4-PSK, 4-QAM | Dibit | 2 | 2N | N |
| 8-PSK, 8-QAM | Tribit | 3 | 3N | N |
| 16-QAM | Quadbit | 4 | 4N | N |
| 32-QAM | Pentabit | 5 | 5N | N |
| 64-QAM | Hexabit | 6 | 6N | N |
| 128-QAM | Septabit | 7 | 7N | N |
| 256-QAM | Octabit | 8 | 8N | N |

Example:

- A constellation diagram consists of 8 equally spaced points on a circle.  If the bit rate is 4800 bps, find the baud .

Sol’n: Constellation indicates 8-PSK (23=8); hence 3 bits are transmitted.

- Find the bit rate for a 16-QAM signal with a band equal to 1000 baud.

16 QAM: 24=16; thus

1000(4) = 4000 bps

- Find the baud for a 72 kbps, 64-QAM signal.

64 QAM: 26=64

IV. Analog-to-Analog Conversion

-AM

-FM

-PM